TR-DLS supported SDRAM module

January 11, 2002

Allen Wang

Friedman Lee

Rev 1.0

- When DIMM is used, please applied it first on DIMM3 then DIMM2, DIMM1, and the last DIMM0 to guarantee the best signal integrity.

- If you can not get DIMM modules list below, the reliability of the system can not be guaranteed (even though the DIMM has the same SDRAM cell but from different DIMM module vendor). Besides, if you indeed want to qualify DIMM module by yourself, the following rules can help you filter out most of the problematic DIMMs.

  - Use x4 cell will be better than x8 cell

  - On the DIMM module, SDRAM clock input (measured on SDRAM cell clock pin) can lead on-DIMM PLL buffer clock input (pin 24 of 2510) from 200ps to 0ps. Register clock input (measured on register cell clock pin) can lead on-DIMM PLL buffer clock input from 300ps to 100ps.

  - The DIMM PCB should follow the standard PCB layout provided by IBM and used by Samsung/Hitachi/Toshiba etc.

  - Make sure your power supply can provide 3.3V or above voltage to the motherboard after installing 4 biggest DIMM modules in your configuration.

| TR-DLS |
| --- |
| Module Supplier | Module P/N | Org (refresh) | DRAM Supplier | Supplier DRAM P/N | Notes | Comment |
| PC133, Reg. SDRAM DIMM 64MB/ 8M x 72 |  |
| Micron | MT9LSDT872G-133C3 GW/ST/T4 | 8Mx8 | Micron | 48LC8M8A2-75C | Speed 133 | - |
| PC133, Reg. SDRAM DIMM 128MB/ 16Mx72 |  |
| Micron | MT9LSDT1672G-133B1 GW/ST/T4 | 16Mx8 | Micron | 48LC16M8A2-75C | Speed 133 | - |
| HITACHI | HB52F169E1-75F | 16Mx4 | Hitachi | 5264405FTT75 | Speed 133 |  |
| SEC | KMM390S1620DT1-C75 | - | SEC | - | Speed 133 | - |
| SEC | KMM390S1620DT1-GA | 16Mx4 | SEC | KM44S16030DT-GA | Speed 133 |  |
| ATP | AR16V72L8S4GAW | 16Mx8 | Winbond | W981208AH-75 | Speed 133 |  |
| ATP | AR16V72L8S4GAS | 16Mx8 | Samsung | K4S280832B-TC75 | Speed 133 |  |
| Apacer | 71.74352.111 | 16Mx8 | Infineon | - | Speed 133 |  |
| Apacer | 75.73352.711 | 8Mx8 | Infineon | HYB39S64800CT-7.5 | Speed 133 |  |
| Century | DTR9A8 | 8Mx8 | Hitachi | 5264805ETT75 | Speed 133 |  |
| Century | DTR9A4 | 16Mx4 | Hitachi | 5264405FTT75 | Speed 133 |  |
| Apacer | 71.74352.461 Low-profile | 16Mx8 | SEC | K4S280832A-TC75 | Speed 133 |  |
| PC133, Reg. SDRAM DIMM 256MB/ 32Mx72 |  |
| Micron | MT18LSDT3272G-133B1 GW/ST/T4 | 32Mx4 | Micron | 48LC32M4A2-75B | Speed 133 | - |
| SEC | KMM390S3320AT1-C75 | - | SEC | - | speed 133 DIMM | - |
| SEC | KMM390S3320BT1-GA | 32Mx4 (mono) |  | KM44S32030BT-GA | speed 133 DIMM Datecode >/=9937 |  |
| ATP | AR32V72L8S8GAS | 32Mx8 | Samsung | K4S560832A-TC75 | Speed 133 |  |
| ATP | AR32V72N4S4GAS | 32Mx4 | Samsung | - | PC-133 |  |
| ATP | AR32V72N4S4GAW | 32Mx4 | Winbond | - | PC-133 |  |
| ATP | AR32V72C4S4GAW | 32Mx4 | Winbond | - | PC-133 |  |
| Century | DTR7E4 | 32Mx4 | Toshiba | TC59SM704FT-75 | Speed 133 |  |
| Apacer | 71.85252.112 | 32Mx4 | Infineon | - | Speed 133 |  |
| Apacer | 71.85252.113 | 32Mx4 | Infineon | - | Speed 133 |  |
| Apacer | 71.85252.462 | 32Mx4 | Samsung | K4S280432B-TC75 | Speed 133 |  |
| Apacer | 71.85352.111 Low-profile | 32Mx8 | Infineon | HYB39S256800AT-7.5 | Speed 133 |  |
| HYUNDAI | HYM71V73C3201 | 32Mx4 (mono) |  | HY57V1294020 TC-75 | speed 133 |  |
| PC133, Reg. SDRAM DIMM 512MB/ 64Mx72 |  |
| SEC | KMM390S6450AT1-C75 | - | SEC | - | speed 133 DIMM | - |
| Century | DTR3S4 | 64Mx4 | Hitachi | 5225405BTT75 | Speed 133 |  |
| Infineon | HYS72V64300GR-7.5-C2 | 64Mx4 | Infineon | HYB39S256400CT-7.5 C2 | Speed 133 | - |
| ATP | AR64V72N4S8GAS | 64M x 4 | - | Speed 133 |  |
| Apacer | 71.96252.112 | 64Mx4 | Infineon | Speed 133 |  |
| Apacer | 71.96252.462 | 64Mx4 | Samsung | Speed 133 |  |
| Hitachi | HB52F649E1-75B | 64Mx4 (mono) | 5225405BTT75 | speed 133 |  |
| PC133, Reg. SDRAM DIMM 1GB/ 128Mx72 |  |
| Hitachi1 | HB52RF1289E2-75B | 64M x 4 stacked | - | Speed 133 | 0 < Ta < 55 |
| IBM | 13M13734BCA-75AY | 64M x 4 stacked | - | Speed 133 | 0 < Ta < 70 |
| SEC | M390S2858AT1-C75 | 64M x 4 stacked | - | Speed 133 | 0 < Ta < 70 |
| Apacer | 71.07257.690 | 64M x 4 stacked | Samsung | Speed 133 | 0 < Ta < 70 |
| Apacer | 71.07257.692 | 64M x 4 stacked | Samsung | Speed 133 | 0 < Ta < 70 |
| ATP | AR128V72N4SSGAS | 64M x 4 stacked | - | Speed 133 | 0 < Ta < 70 |
| Noted: most of current 1GB DIMMs use “stacked” structure which incurs serious memory thermal concern. Be remember to provide adequated air-flow through the memory subsystem. Also, please measure the temperature on those DIMMs in your system configuration and make sure they are always under the maximum allowable working temperature. |

Note 1.	Hitachi 1GB/HB52RF1289E2-75B must have good air flow due to its limited Ta.