### Release Note:  618-20902-4403-CX1

- Initial Release of MODS_2003_0902 “40.44.3” “X” State Manufacturing Diagnostics for engineering

evaluation with E133MFT and E133MFG batch files for Asus/L5G laptop, NV31-464 MFC,31 chip solder

down config.

Test Instruction:

-   For FCT:

*  Connect CRT, and STV out cables  then run "E133CMFT.BAT".

Follow the instructions display on screen.

-   For OQA:

* Connect CRT  then run "E133MFG.BAT".

- Note:

  - Golden value was successfully generated by  PVS

-     The guardband set at  282/306 (nv/mclk) with actual reading are 282.1/306.

  - Power_mizer 2 = 201/201 (nv/mclk).

  - Power_mizer 1 = 100/100 (nv/mclk).

Validated by: DucT.           Verified by: Lay.Y (Sept.03.03)

- Removed all other files associated with other PCBAs.

PCBA Test Coverage

Asus /L5G, E133(MAP31-464 module), DID= 31b, GForce FX  Go5650,  SiRev=A1, 64 MB DDR,

SVID = 1043, SDID = 1771, VBIOS: 4.31.20.64.07 (E133.rom), 276/301 (nv/mclk) ,Shelley ‘s Laptop

Asus-L5G-!Asku04,  tracking ID#005257.

Chipset Test Coverage

Intel 8086  Springdale

Display Test Coverage

LCD (XGA 10x7).

CRT

#### TV