L7000 Series Notebook CPU Insertion/Extration Tools User Guide

1. Specifications:

  - Applied for : ASUSTek. L7000 series Notebook

  - Dimensions：270mm(L)×100mm(W)×23mm(H)

  - Material：POM(White)、Stainless Steel

  - Appearance：As shown in the pictures.

- Supporting Frame     d. Pulling Handle (White)

- Releasing Hook       e. Handle (White)

- Adjustment Screw     f. Handle Screw

  - Stroke：The distance between the top position of Releasing Hook and the Supporting Frame is D= 6.0mm±0.2mm, as shown in Pic. 1.

  - All rights reserved. Do not copy.

2. Preparation & Calibration：

Before using this tool, make sure the working environment is under Anti-Static Protections. Check if there is any bending, deformation, or damage in any part of the unit, especially in the supporting frame and the releasing hook.

Make sure the stroke of the unit complies with the standard ( D=6.0mm±0.2mm ). Follow the operation instructions while using it. Note that this tool is simply offered to provide a convenient way of inserting and extracting Notebook CPU. ASUSTek will not be responsible for any damage caused by any misusage of this unit.

- Stroke Calibration (already calibrated in factory)

  - Calibration of Releasing Hook stroke: Release the handle screw and remove the handle. (Pic.2)

  - Adjust the screw as shown in Pic. 3 to make D=6.0mm±0.2mm (Default).

4. Operation Instructions：

  - CPU extraction

    - Insert the extraction tool into the Extraction Position (2) as shown in Pic.5. Keep the tool in vertical position.

    - Pull the handle to lift CPU.

    - Remove the CPU.

  - CPU insertion

    - Place the CPU on top of the very position of main board. Make sure three of the CPU screw holes are aligned to the screw fixtures of the main board.

    - Use the insertion tool to apply force on the Insertion Position (1) as shown in Pic. 4. Make sure the CPU is fully inserted into the connector.

# Text boxes

e.

f.

d.

c.

b.

a.

Pic. 1. The distance between the top position of Releasing Hook and the Supporting Frame is

D= 6.0mm±0.2mm

Pic. 2.  Release the Handle Screw and remove the Handle.

Pic. 4.  CPU insertion tool,

Insertion Position (1)

Pic. 3.  Calibrate the Adjustment Screw

Pic. 5.  CPU extraction tool,  Extraction Position (2)