# Remarks on Test Results

Test System……….. ASUS MDC Notebook

## Test MR…………… HSP56 MR

OSs..………………. Windows 98/Millennium/Windows 2000

Apps..………………HCT 9.6/HCT 9.502

MR Driver…………R2.30B2022/R2.30B2022/R2.30B2022(data/fax/voice)

- INFCATREADY

Ran the latest INFCATR for the MR drivers and generated their signability text file which is placed in a separated folder \Signability under \Test_Log on the submission CD

2.   MCT for Windows Millennium

MCT V.250 Tests

### AT + GCI:  the test got warning but it is no longer required per

### modem errata #266

### http://www.microsoft.com/hwtest/search/details.asp?Type=Errata&ID=266&Key=modem&Sort=Title

MCT Interactive Tests

Speaker Volume: This modem supports volume On and Off only and so Speaker

Volume Low/Med/High test will be skipped and logged

as Pass by MCT

Blind Dial: It does not generate any tone when the phone line is

unplugged.   This is because the Silicon DAA is powered by

the line current.   One way to verify blind dial is to use TAS

Series 2 and disable the dial tone frequency while still

providing the line current

MCT Voice Tests

HandsetHookSwitch

&HandsetAudio: the test modem does not support handset and it has been

disabled in Voice Profile in the INF file.    Therefore, the two

tests are skipped and logged as Pass by MCT

SpeakerphoneHook

Switch&Speaker-

phoneVolumeGain: the modem driver does not support speakerphone.

#### Therefore, the two tests are skipped and logged as Pass by

MCT

3.   PCI Latency Test in Windows 2000

The test was not performed since it has been removed from all tester types (refer to WHQL July 24, 2000 announcement)