HSP Modem( Technology

#### ASUS MDC

HSP56 MR

Installation

Manual

June 1, 2000

Table of Contents

| Section 1 |  |  |
| --- | --- | --- |
| 1.0 | Introduction | Page 1 |
| 1.1 | System Requirements | Page 1 |
| 1.2 | Features | Page 1 |
| Section 2 |  |  |
| 2.0 | HSP56 MR Setup and Software Installation |  |
|  | Windows 95 Windows 98 Windows NT 4.0 Windows 2000 Windows Millennium (WDM) | Page 2 Page 5 Page 8 Page 11 Page 14 |

# Section 1

## 1.0 Introduction

This document provides reference information for the testing of HSP56 MR based on Host Signal Processing (HSP) Data/Fax/Voice/Speakerphone Modem Technology. The HSP Modem Riser™ eliminates the redundant hardware parts found in most modems today. These include the data pump, a controller, an additional UART and external memory as required in a conventional approach. In addition, the complete HSP solution allows an internal modem to be upgraded with enhancements and features through software upgrades rather than a chip change or board swap.

## 1.1 System Requirements

- Intel Pentium 166 MHz  + (includes Pentium MMX, Pentium II, and Pentium III)

- AMD K6 200 MHz + (includes AMD-K6-2, AMD-K6-III, and AMD-K7)

- Cyrix 6x86MX PR233 MHz + (includes Cyrix M II)

- 16MB RAM (32MB RAM required for Windows 2000)

- Windows 95 (Includes OSR1/OSR2), Windows 98 (Includes Second Edition), Windows NT 4.0, Millennium, Windows 2000.

## 1.2 Features

DATA

Supported Communication Standards

V.90, *K56Flex, V.34, V.32bis, V.32, V.22bis, v.22, V.21, V.23, Bell212A, Bell 103

Data Compression

V.42bis

Error Correction

V.42 LAPM

FAX

Supported Protocols

V.8bis, V.80, V.17, V.29, V.27ter, V.21 Channel 2

General Features

Auto Fallback

AT Commands

PCI Bus interface

Data/Fax

Signal Quality Monitoring and Auto Retrain

Operating System Compatibility

Windows 95 OSR1/OSR2

Windows NT 4.0

K56Flex is a registered trademark of Rockwell and Lucent Technologies.

MNP 5

MNP 2,3,4

EIA Class 1

Low power consumption

Auto Selection of COM Port and IRQ settings

High throughput Virtual UART, DTE  rate up

to 115,200

Windows 98/Millennium

Windows 2000

Windows is a registered trademark of Microsoft Corp.

# Section 2

## 2.0	HSP56 MR Setup using Windows 95 OEM Service Release 2

The HSP modem driver will automatically handle all variations of MMX-capable CPU types.  This eliminates the problem of poor performance that results from installing the incorrect driver.  The driver will take advantage of the MMX enhancements.

- If another HSP modem driver was previously installed, be sure to remove the software by following the appropriate Uninstallation Procedure provided in the prior manual.

When the computer is turned off, plug the HSP56 MR modem card into the MR slot.  After the system is turned on, it will automatically detect the MR card.  The installation program will begin with the screen shown below.  At this point, insert the HSP56 MR driver CD-ROM in the CD-ROM drive and click “Next”.  Follow the “Wizard” installation instructions.

2.	Click “Other Locations…” in the Update Device Driver Wizard to install the driver from CD.

3.    Type “D:\WIN9XNT4” (where D: is the CD-ROM Drive) in the Location field and click “OK”.

- Type “D:\WIN9XNT4” (where D: is the CD-ROM Drive) in the prompted field and click “OK” to complete the installation.

- After the installation is complete, the following modem listing should be shown under “Modem Properties” in the “Control Panel”.

Uninstallation:

The HSP56 MR can be uninstalled by using the following procedure.

- Double-click “Add/Remove Programs” under “Control Panel”.

- Select “HSP56 MR Drivers” and click “Add/Remove”.  The uninstallation program will automatically remove the HSP Modem from the system.

HSP56 MR Setup using Windows 98

The HSP modem driver will automatically handle all variations of MMX-capable CPU types. The driver will take advantage of the MMX enhancements.

- If another HSP modem driver was previously installed, be sure to remove the software by following the appropriate Uninstallation Procedure provided in the prior manual.

When the computer is turned off, plug the HSP56 MR into the MR slot.  When the system is turned on, it will automatically detect the MR card.  The installation program will begin with the screen shown below.  At this point, insert the HSP56 MR driver CD-ROM in the CD-ROM drive and click “Next”. Follow the “Wizard” installation instructions.

- Windows will search for the driver.  Choose the “Recommended” option and click “Next”.

- Choose “Specify a location” and type “D:\WIN9XNT4” (where D: is the CD-ROM Drive) in the prompt field.  Click “Next” and continue to follow the “Wizard” instructions to complete the installation process.

- After the installation is complete, the following modem listing should be shown under “Modem Properties” in the “Control Panel”.

Uninstallation:

The HSP56 MR can be uninstalled by using the following procedure.

1.	Double-click “Add/Remove Programs” under “Control Panel”.

- Select “HSP56 MR Drivers” and click “Add/Remove”.  The uninstallation program will automatically remove the HSP Modem from the system.

HSP56 MR Setup using Windows NT Workstation 4.0

If another HSP modem driver was previously installed, be sure to remove the software by following the appropriate Uninstallation Procedure provided in the prior manual.

- Insert the HSP56 MR driver CD-ROM and select “Run” under the “Start” menu.  Type the path as shown below to start the installation and click “OK”.  Note that D: is the CD-ROM drive letter.

- Click “Next” to continue the installation program.

- Click “Finish” to continue.

7.	After installation, the following modem should be listed under “Modem Properties” in the “Control Panel”.

Uninstallation:

The HSP56 MR can be uninstalled by using the following procedure.

- Double-click “Add/Remove Programs” under “Control Panel”.

- Select “HSP56 MR Drivers” and click “Add/Remove”.  The uninstallation program will automatically remove the HSP Modem from the system.

HSP56 MR Setup using Windows 2000

If upgrading from a previous Operating System (i.e. NT4), the previous HSP56 MR driver must be removed before loading Windows 2000 Operating System by following the appropriate Uninstallation Procedure provided in the previous pages.

1. When the computer is turned off, plug the HSP56 MR modem into the MR slot.  When the system is turned on, it will automatically detect the MR card.  The installation program will begin with the screen shown below.  Select “Search for a suitable driver for your device” and click “Next”.

- Under “Optional search locations”, check “Specify a location” and leave other options unchecked.  At this point, insert the HSP56 MR driver CD in the CD-ROM drive and click “Next”.

- Type “D:\WIN2000” (where D: is the CD-ROM Drive) in the prompted field and click “OK” to continue the installation.

- Click “Next” to continue the installation when Windows 2000 has found the driver on the disk.

- After Windows 2000 has finished copying the driver files, click “Finish”.

Uninstallation:

The HSP56 MR can be uninstalled by using the following procedure.

- Double-click “Add/Remove Programs” under “Control Panel”.

- Select “HSP56 MR Drivers” and click “Change/Remove”.  The uninstallation program will automatically remove the HSP Modem from the system.

HSP56 MR Setup using Windows Millennium WDM

The HSP modem driver will automatically handle all variations of MMX-capable CPU types. The driver will take advantage of the MMX enhancements.

- If another HSP modem driver was previously installed, be sure to remove the software by following the appropriate Uninstallation Procedure provided in the prior manual.

When the computer is turned off, plug the HSP56 MR into the MR slot.  When the system is turned on, it will automatically detect the MR card.  The installation program will begin with the screen shown below.  At this point, insert the HSP56 MR driver CD-ROM in the CD-ROM drive and click “Next”. Follow the “Wizard” installation instructions.

2.) 	Windows will search for driver. Choose the “Recommended” option and choose “Specify a location and type “D:\WDM” (where D: is the CD-ROM Drive) in the prompt field. Click “Next” and continue to follow the “Wizard” instructions.

3.	Windows founded the driver for the modem, Click “Next” to continue the “Wizard” Process.

4. 	Windows has finished installing the WDM driver. Click “Finish” to finish the installation process.

5.	After the Installation is complete, the following modem listing should be shown under “Modem Properties” in the “Control Panel”.

Uninstallation:

The HSP56 MR can be uninstalled by using the following procedure.

1.	Double-click “Add/Remove Programs” under “Control Panel”.

- Select “HSP56 MR Drivers” and click “Add/Remove”.  The Uninstallation program will automatically remove the HSP Modem from the system.

# Text boxes

HSP56 MR

PCI Card

PCI Card

HSP56 MR